## Slide 1: Advanced Robot Programming

## Slide 2
Table of Content
TCP/IP commander cmd_vel
TCP/IP listener scan
TCP/IP listener odom
Shared memory and semaphores
Position and orientation of the robot
Programm to move the robot on a given path

## Slide 3
TCP/IP commander cmd_vel
void cmd_vel(float linear, float angular) {
// Establish a connection to the server on port 9999
connection(9999);
// Wait for the semaphore
sem_wait(sem);
char command[100];
// Format the command with linear and angular values
snprintf(command, sizeof(command), "---START---{\"linear\":%f , \"angular\":%f}___END___", linear, angular);
std::string formattedCommand = std::string(command);
// Use the formatted string in the subsequent code
if (send(sock, formattedCommand.c_str(), formattedCommand.length(), 0) != formattedCommand.length()) {
sem_post(sem); // Release the semaphore in case of an error
DieWithError("Error sending message");
}
// Release the semaphore after sending the message
sem_post(sem);
// Disconnect from the server on port 9999
disconnect(9999);
}

## Slide 4
TCP/IP listener scan
char *scan() {
connection(9997);
if (is_Test==0){
message("---START---{\"header\": {\"seq\": 20550, \"stamp\": {\"secs\": 1677514522, \"nsecs\": 217517053}, \"frame_id\": \"base_scan\"},\"angle_min\": 0.0, \"angle_max\": 6.2657318115234375, \"angle_increment\": 0.01745329238474369, \"time_increment\": 0.0005592841189354658, \"scan_time\": 0.20134228467941284, \"range_min\": 0.11999999731779099, \"range_max\": 3.5, \"ranges\": [0.0, 0.0,0.0, …], \"intensities\": [0.0, 0.0, 170.0, …]}___END___");
}
if (is_Test == 1) {
message(".");
}
// Receive data from the server with a maximum data size of 8000
Char *receivedData = receive(8000);
// Write the received data to shared memory
sem_wait(sem);
strcpy(echoBuffer, receivedData);
sem_post(sem);
// Disconnect from the server on port 9997
disconnect(9997);
return receivedData;
}

## Slide 5
TCP/IP listener odom
char *odom() {
connection(9998);
if (is_Test==0){
message("---START---{\"header\": {\"seq\": 96997, \"stamp\": {\"secs\": 1677514236, \"nsecs\": 463284111}, \"frame_id\": \"odom\"}, \"child_frame_id\":\"base_footprint\", \"pose\": {\"pose\": {\"position\": {\"x\": 0.45223192989826202, \"y\": 0.86337219601869583, \"z\": 0.0}, \"orientation\": {\"x\": 0.0, \"y\": 0.0, \"z\": -0.965720534324646, \"w\": 0.2595840394496918}}, \"covariance\": [0.0, 0.0, 0.0, 0.0, 0.0, 0.0, 0.0, 0.0, 0.0, 0.0, 0.0, 0.0, 0.0, 0.0, 0.0, 0.0, 0.0, 0.0, 0.0, 0.0, 0.0, 0.0, 0.0, 0.0, 0.0, 0.0, 0.0, 0.0, 0.0, 0.0, 0.0, 0.0, 0.0, 0.0, 0.0, 0.0]}, \"twist\": {\"twist\": {\"linear\": {\"x\": -0.0007909589330665767, \"y\": 0.0, \"z\": 0.0}, \"angular\": {\"x\": 0.0, \"y\": 0.0, \"z\": -0.0019147992134094238}}, \"covariance\": [0.0, 0.0, 0.0, 0.0, 0.0, 0.0, 0.0, 0.0, 0.0, 0.0, 0.0, 0.0, 0.0, 0.0, 0.0, 0.0, 0.0, 0.0, 0.0, 0.0, 0.0, 0.0, 0.0, 0.0, 0.0, 0.0, 0.0, 0.0, 0.0, 0.0, 0.0, 0.0, 0.0, 0.0, 0.0, 0.0]}}___END___; }
if (is_Test == 1) {
message(".");
}
char *receivedData = receive(1000);
// Write the received data to shared memory
sem_wait(sem);
strcpy(echoBuffer, receivedData);
sem_post(sem);
// Disconnect from the server on port 9998
disconnect(9998);
return receivedData;
}

## Slide 6
Shared memory and semaphores
void init_shared_memory() {
// Create or open a shared memory segment and obtain a file descriptor
int fd = shm_open("/my_shared_memory", O_CREAT | O_RDWR, S_IRUSR | S_IWUSR);
// Set the size of the shared memory segment
ftruncate(fd, RCVBUFSIZE);
// Map the shared memory segment into the process's address space
echoBuffer = static_cast<char *>(mmap(NULL, RCVBUFSIZE, PROT_READ | PROT_WRITE, MAP_SHARED, fd, 0));
// Close the file descriptor after mapping
close(fd);
// Open or create a semaphore for synchronization
sem = sem_open("/my_semaphore", O_CREAT, S_IRUSR | S_IWUSR, 1);
if (sem == SEM_FAILED) {
DieWithError("sem_open() failed");
}
}
void close_shared_memory() {
// Unmap the shared memory segment from the process's address space
munmap(echoBuffer, RCVBUFSIZE);
sem_close(sem);
// Remove the shared memory segment
shm_unlink("/my_shared_memory"); // Remove the semaphore
Sem_unlink("/my_semaphore");
}

## Slide 7
Position and orientation of the robot
Odometry data
AddtoOdomData
  extract specific values from the provided data based on the desired data types and stores them in the odomData array. The extracted values are associated with their respective keys, and the number of entries is incremented accordingly.
extractOdomData
  extract specific data related to position, orientation, linear, and angular values
  add them to the odomData array.
  It checks for start and end markers in the message and handles errors if markers are missing.
processOdomData
  process odometer data by repeatedly extracting and printing information until the end of the message.
  It handles cases where start and end markers are missing and provides appropriate error messages.

## Slide 8
Position and orientation of the robot
Laserscan data
AddRanges
  adds range data to the scanData array, selecting data points based on a specified degree interval.
  It creates key strings based on the degree of the corresponding data point and stores the range value along with the key in the array. The function increments the number of entries in the scanData array accordingly.
extractRangeData
  extract range data from a message, tokenize the data, and store it in a structure.
  It handles cases where start and end markers are missing, providing an appropriate error message.
processScanData
  processes scan data received from the server, extracting range data, adding it to the scanData array, and displaying the results.
  It handles multiple scan messages in the message stream, and appropriate error messages are displayed if delimiters are missing.

## Slide 9
Programm to move the robot on a given path
MoveRobot_linear
  move the robot linearly by a specified distance by calculating the required speed and sends velocity commands.
  Use the robot's position with odometry data, and updates a boolean to indicate when the movement is finished.
MoveRobot_circular
  move the robot in a circular path with a specified radius by calculating linear and angular speeds and sends velocity commands.
  Use the robot's position with odometry data, and updates a boolean to indicate when the movement is finished.
Move_path
  defines a sequence of robot movements based on user input and performs the movements accordingly.
  It involves linear and circular motions, pauses, and updates based on the robot's orientation and position.

## Slide 10: Live demonstration

## Slide 11: QnA